## Slide 1: Fortran for programmers
Geert Jan Bex (geertjan.bex@uhasselt.be)
Acknowledgement: many thanks to Reinhold Bader (LRZ, Garching) for suggestions & corrections
License: this presentation is released under the Creative Commons CC BY 4.0, see https://creativecommons.org/licenses/by/4.0/deed.ast

## Slide 2
http://bit.ly/2pvYPPu

## Slide 4: Fortranosaurus?
There are only two kinds of programming languages, theones people complain about and the ones nobody uses.
— Bjarne Stroustrup

## Slide 5: Introduction
Fortran & LISP were first high-level programming languages
Fortran versions still around
  Fortran 77
  Fortran 90
  Fortran 95
  Fortran 2003
  Fortran 2008
Fortran is still very relevant
  language with many modern features, e.g., object orientation
  clear semantics, easy to optimize
  excellent language for scientific computing
  good quality compilers (Intel, PGI,…)
  lots of legacy code

## Slide 6: Typographic conventions for slides
Code is set in Courier New
Fortran keywords, intrinsic functions,… are in upper case
  they need/should not be in actual Fortran code, Fortran is not case-sensitive
Good practice:
(Potential) hazards/bugs:
Performance issue:
Compare with C/C++:
C/C++

## Slide 7: Slides & sample code
Available online, public domain
  https://gjbex.github.io/Fortran-for-programmers/
  License: https://creativecommons.org/licenses/by/4.0/deed.ast
Clone the repository or download ZIP
  This presentation
  Subdirectories with code illustrations will be mentioned in slides at appropriate places
  Hands-on material

## Slide 8: Code format & program structure
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/Miscellaneous

## Slide 9: Free source form
Fortran 77 had column format
Fortran 90+ allows for free source form
PROGRAM free_source_form
INTEGER :: i
INTEGER, PARAMETER :: n = 10
! This will print something to screen
DO i = 1, n
PRINT '(A, I2, A, I2)', &
'This is iteration ', i, &
' out of ', n
END DO
END PROGRAM free_source_form
comment
arbitrary indentation
Fortran is not case-sensitive!
C/C++
line continuations
C/C++

## Slide 10: Program unit structure
(Almost) same for PROGRAM, SUBROUTINE, FUNCTION, MODULE (see later)
PROGRAM program_structure
INTEGER :: i
INTEGER, PARAMETER :: n = 10
DO i = 1, n
PRINT '(A, I2, A, I2)', &
'This is iteration ', i, &
' out of ', n
END DO
CALL my_subroutine(n)
CONTAINS
…
END PROGRAM program_structure
variable declarations
statements
internal procedure definitions
start of unit
end of unit

## Slide 11: Basic data types
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/Types

## Slide 12: Implicit types
Convention: type based on first character of variable name
  'i' to ‘n': INTEGER
  'a' to 'h', ‘o' to 'z': REAL or DOUBLE PRECISION
Advantage: saves typing, no need to declare variables
Disadvantage: no need to declare variables
  mistakes likely

## Slide 13: No implicits
Always use IMPLICIT NONE
  variables must be declared explicitly
  in PROGRAM, MODULE, SUBROUTINE, FUNCTION
  example:
MODULE math_funcs
USE iso_fortran_env
IMPLICIT NONE
INTEGER :: i
…
END MODULE math_funcs

## Slide 14: Fortran 90 versus Fortran 95+
Integers
  4 byte: INTEGER*4 vs. INTEGER(KIND=4)
  8 byte: INTEGER*8 vs. INTEGER(KIND=8)
Real numbers
  single precision: REAL vs. REAL(KIND=4)
  double precision: DOUBLE PRECISION vs. REAL(KIND=8)
Still not portable!

## Slide 15: Platform independence
Use
  SELECTED_INT_KIND(r=…)
  SELECTED_REAL_KIND(p=…, r=…)
…
INTEGER, PARAMETER :: sp = SELECTED_REAL_KIND(p=6, r=30), &
dp = SELECTED_REAL_KIND(p=12, r=100), &
int = SELECTED_INT_KIND(r=8), &
long = SELECTED_INT_KIND(r=20)
REAL(KIND=sp) :: x
REAL(KIND=dp) :: y
INTEGER(KIND=int) :: m
INTEGER(KIND=long) :: n
x = 1.0_sp/3.0_sp
n = 2_long**40_long
…
range: store integer of at least
range: store real of at least
precision: store at least p digits

## Slide 16: Alternative kinds
Use iso_fortran_env module
  INT8, INT16, INT32, INT64
  REAL32, REAL64, REAL128
…
USE, INTRINSIC :: iso_fortran_env
INTEGER, PARAMETER :: sp = REAL32, &
dp = REAL64, &
int = INT32, &
long = INT64
REAL(KIND=sp) :: x
REAL(KIND=dp) :: y
INTEGER(KIND=int) :: m
INTEGER(KIND=long) :: n
x = 1.0_sp/3.0_sp
n = 2_long**40_long
…
not supported by all compilers, potentially (very) slow
if something shouldn't
change, make sure it doesn't: PARAMETER

## Slide 17: Basic types
Floating point numbers
  REAL(KIND=REAL32)
  REAL(KIND=REAL64)
Complex numbers
  COMPLEX(KIND=REAL32)
  COMPLEX(KIND=REAL64)
Integers
  INTEGER(KIND=INT32)
  INTEGER(KIND=INT64)
Boolean values
  LOGICAL: .TRUE., .FALSE.
Characters & strings
  CHARACTER
  CHARACTER(LEN=…)

## Slide 18: Type conversions & KIND function
Intrinsic functions for type conversion
  REAL, INT, use KIND optional argument to control precision
  CMPLX(re, im)
Specify specific kind in conversion functions
…
REAL(KIND=dp) :: y
REAL(KIND=sp) :: result
REAL(KIND=sp), DIMENSION(n) :: x
INTEGER :: i
…
DO i = 1, SIZE(x)
y = REAL(x, KIND=KIND(y))) + f(REAL(i, KIND=KIND(y)))
…
END DO
result = y
…
ensure computation is done in same precision as y

## Slide 19: Numerical models
Largest number for type
  HUGE(INT(0, KIND=INT32))
  HUGE(REAL(0.0, KIND=REAL64))
Smallest number > 0 for type
  TINY(REAL(0.0, KIND=REAL32))
Smallest number  such that 1 +  > 1
  EPSILON(REAL(0.0, KIND=REAL64))
Decimal precision
  PRECISION(REAL(0.0, KIND=REAL32))
Range of exponents 10r
  RANGE(REAL(0.0, KIND=REAL64))
  RANGE(INT(0, KIND=INT64))
0
1
TINY
1 + EPSILON
HUGE

## Slide 20: Values for real & integer types
 | REAL32 | REAL64 | REAL128
HUGE | 3.40282347E+38 | 1.7976931E+308 | 1.1897315E+4932
TINY | 1.17549435E-38 | 2.2250739E-308 | 3.3621031E-4932
EPSILON | 1.19209290E-07 | 2.2204460E-016 | 1.9259299E-0034
RANGE | 37 | 307 | 4931
PRECISION | 6 | 15 | 33
 | INT8 | INT16 | INT32 | INT64
HUGE | 127 | 32767 | 2147483647 | 9223372036854775807
RANGE | 2 | 4 | 9 | 18

## Slide 21: Infinity & NaN
Floating point numerical overflow
  very_large + even_larger Infinity
  largish**smallish  Infinity
  LOG(very_small)  -Infinity
Illegal floating point operations
  0/0  NaN
  SQRT(-1.0)  NaN
NaN = Not a Number
…
REAL(KIND=dp) :: huge_dp = HUGE(0.0_dp)
REAL(KIND=dp) :: x
…
IF (x > huge_dp .OR. x < -huge_dp) …
…
IF (x /= x) …
…
is infinity?
is NaN?

## Slide 22: Better infinities & NaNs
If implemented, use ieee_arithmetic module
…
USE, INTRINSIC :: ieee_arithmetic
…
REAL(KIND=dp) :: huge_dp = HUGE(0.0_dp)
REAL(KIND=dp) :: x
…
IF (.NOT. IEEE_IS_FINITE(x)) …
…
IF (IEEE_IS_NAN(x)) …
…
IF (.NOT. IEEE_IS_NORMAL(x)) …
…
is finite?
is NaN?
is finite and not NaN?
Okay for Intel 14.x & GCC 5.x

## Slide 23: Functions & arithmetic operators
Operators: +, -, *, /, **
  Work on INTEGER, REAL, COMPLEX of all kinds
  No surprises, except integer division: 3/5 == 0
Functions
  SQRT, SIN, COS, TAN, ASIN, ACOS, ATAN, SINH, COSH, TANH, EXP, LOG, LOG10,…
  MOD
  FLOOR, CEILING, NINT
  MIN, MAX

## Slide 24: Strings
Character & string constants
  use either single, or double quotes
String declaration: specify length
String concatenation: // operator
String procedures
  comparing strings: LGT, LGE, LLT, LLE, ==, /=
  remove trailing whitespace: TRIM
  find substring: INDEX
…
INTEGER, PARAMETER :: max_len = 80
CHARACTER(LEN=max_len) :: message = 'OK'
Fortran is not your friend for string processing!
Improved though: CHARACTER(LEN=:), ALLOCATABLE :: ds

## Slide 25: Control constructs
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/ControlStructures

## Slide 26: Conditional statements: IF
Block if statement
Logical if statement
…
IF (x > 10.0) THEN
…
ELSE
…
END IF
…
relational operators: ==, /=, <, <=, >, >=
…
IF (x > 10.0) …
…
Note: - one statement, not a block - no ELSE
- no END IF
logical operators:
.AND., .OR., .NOT.
logical values:
.TRUE. and .FALSE.

## Slide 27: Conditional statements: SELECT
Select case block
…
CHARACTER(LEN=1) :: operator
…
SELECT CASE (operator)
CASE ('+')
PRINT "(I3, A2, I3, ' = ', I6)", a, operator, b, a + b
CASE ('*')
PRINT "(I3, A2, I3, ' = ', I6)", a, operator, b, a * b
CASE DEFAULT
PRINT "('# error: unknown operand ''', A, '''')", operator
END SELECT
…
types: CHARACTER, INTEGER
Note semantic difference with C/C++:
cases are exclusive, no break needed
C/C++

## Slide 28: Conditional statements: WHERE
Where block, conditions on array elements
…
REAL(KIND=sp), DIMENSION(m, n) :: A LOGICAL, DIMENSION(m, n) :: pos, neg, zero
…
pos = .FALSE.
neg = .FALSE.
zero = .FALSE.
WHERE (A < -1.0e-5_sp)
neg = .TRUE.
ELSEWHERE (A > 1.0e-5_sp)
pos = .TRUE.
ELSEWHERE
A = 0.0_sp
zero = .TRUE.
END WHERE
…

## Slide 29: Conditional function: MERGE
Merge function returns value based on condition
cfr. ternary operator: … ? … : …
C/C++
…
IF (x > 10.0) THEN
y = 5.0
ELSE
y = 0.5
END IF
…
…
y = MERGE(5.0, 0.5, x > 10.0) …

Can be used with arrays,
similar to WHERE

## Slide 30: Iteration statements: DO
Do block
…
INTEGER :: i, initial, final, step
…
DO i = 1, 10
…
END DO
…
PRINT *, i
…
DO i = initial, final, step
…
END DO
…
type must be INTEGER
value of i will be 11

## Slide 31: Iteration statements: DO WHILE
Do while block
…
REAL(KIND=dp) :: x
…
x = 5.0_dp
DO WHILE (x > 0.0_dp)
…
x = x - 0.1_dp
END DO
…

## Slide 32: EXIT and CYCLE
In do and do while constructs
  EXIT: stop iterating
  CYCLE: skip remainder of block, execute next iteration
  permits execution control in nested constructs (see later)!
…
DO i = 1, n
IF (is_prime(i)) CYCLE
IF (is_enough(i)) EXIT
CALL compute_some_stuff(i, alpha)
END DO
…

## Slide 33: Iteration statements: FORALL
Forall block, conditions on indices
INTEGER, PARAMETER :: n = 5
REAL(KIND=dp), DIMENSION(n, n) :: a
INTEGER :: i, j
…
a = 0.0_dp
FORALL (i = 1:n, j = 1:n, i == j - 1 .OR. i == j + 1)
a(i, j) = 1.0_dp
END FORALL
…
…
FORALL (i = 1:n, j = 1:n, a(i, j) < 0.0)
a(i, j) = 0.0
END FORALL
…
use WHERE
Execution of iterations not necessarily in order
Complex expressions:
temporary arrays are created

## Slide 34: BLOCK construct
Allows local scoping
…
INTEGER :: i, n
…
DO i = 1, n
BLOCK
REAL(KIND=dp) :: frac
frac = 1.0_dp/i
…
END BLOCK
END DO
…
procedure-scoped variables
local variable, only declared within
BLOCK

## Slide 35: ASSOCIATE construct
Allows aliasing of subarrays, parts of user defined types, or expressions
…
REAL(KIND=dp), DIMENSION(m, n) :: data_array
…
DO i = 1, m
ASSOCIATE( row => data_array(i, :) )
row = update(row)
…
END ASSOCIATE
END DO
…
local name, no declaration, only alias within
ASSOCIATE
Helps to write code that is easier to read

## Slide 36: Named blocks
Improves code readability
Helps compiler catch semantic mistakes
outer: DO j = 1, n
…
inner1: DO i = 1, m
…
END DO inner1
…
inner2: DO i = 1, m
…
IF (…) EXIT outer
END DO inner2
…
END DO outer
Works for all block statements:
IF, SELECT CASE, WHERE, DO, DO WHILE, FORALL, BLOCK
can be used to EXIT/CYCLE from/to the desired loop level

## Slide 37: STOP statement
Statement halts execution, returns exit code, or string
…
IF (x < 0.0) THEN
STOP 'x must be positive'
END IF
…
Note: exit code is 0!
USE, INTRINSIC:: iso_fortran_env, ONLY : error_unit
…
INTEGER, PARAMETER :: real_err_exit = 1
…
IF (x < 0.0) THEN
WRITE (UNIT=error_unit, FMT='(A)'), 'x must be positive'
STOP real_err_exit
END IF
…

## Slide 38: Arrays
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/Matrices

## Slide 39: Array declaration & initialization
Statically declared
Initialization & reshaping
…
REAL(KIND=dp), DIMENSION(100) :: v, w …
INTEGER, PARAMETER :: m = 2000, n = 1000
INTEGER, DIMENSION(m, n) :: A, B
…
…
v = 1.0_dp
w = [ (SQRT(REAL(i, KIND=dp)), i = 1, 100) ]
…
A = 0
B = RESHAPE([ ((i*n + j, i = 0), m - 1), j = 1, n) ], [m, n])
…

## Slide 40: Array indexing
Indices run from 1 to array size for each dimension (unless declared otherwise)
…
REAL(KIND=dp), DIMENSION(100) :: v
REAL(KIND=dp) DIMENSION(100, 200) :: A …
DO i = 1, 100
CALL something(v(i))
END DO
DO i = 1, 100 DO j = 1, 200
CALL something_else(A(i, j))
END DO
END DO
…
A(3, 5) = 3.0_dp*A(7, 21) + v(13)
…
C/C++
cfr. C: 0 to size-1

## Slide 41: Array storage
Array elements are stored column-wise
…
DO j = 1, SIZE(A, 2)
DO i = 1, SIZE(A, 1)
… A(i, j) …
END DO
END DO
…
Remember: arrays are stored by column
determine dimensions at run time
Note difference with C/C++:
arrays are stored by row
C/C++

## Slide 42: Array indexing: custom bounds
Lower and upper index can be any number
…
REAL(KIND=dp), DIMENSION(-100:100) :: v
REAL(KIND=dp), DIMENSION(0:5, 1:200) :: A …
DO i = LBOUND(v), UBOUND(v)
CALL something(v(i))
END DO
DO j = LBOUND(A, 2), UBOUND(A, 2) DO i = LBOUND(A, 1), UBOUND(A, 1)
CALL something_else(A(i, j))
END DO
END DO
…
A(0, 5) = 3.0_dp*A(5, 21) + v(-13)
…
determine dimensions at run time
Don't overuse!

## Slide 43: Array indexing: slicing
…
INTEGER, PARAMETER :: m = 4, n = 5
INTEGER, DIMENSION(m, n) :: A = RESHAPE([(i, i=1, m*n)], [m, n])
INTEGER, DIMENSION(m/2, n/2) :: B …
A(2:m-1, 2:n-1) = 0
…
1 5 9 13 17
2 6 10 14 18
3 7 11 15 19
4 8 12 16 20
…
r3_sum = SUM(A(3, :))
c4_sum = SUM(A(:, 4))
…
22
29
1 5 9 13 17
2 0 0 0 18
3 0 0 0 19
4 8 12 16 20
…
B = A(1:m:2, 2:n:3)
…
5 17
0 19
lower bound
upper bound
stride
all: ( : )
up to: ( :upper)
from: (lower: )
from, up to: (lower: upper)
all with stride: ( : : stride)
from, up to, stride: (lower:upper:stride)

## Slide 44: Array operations
Scalar-array: +, -, *, /, **
  2.0_dp + A: add 2.0 to each array element
  3.0_dp*A: multiply each array element by 3.0
Element-wise array-array: +, -, *, /, **
  A = B + C: sum
  A = B*C: element-wise product
Vector-vector product:
  u = DOT_PRODUCT(v, v)
Matrix-matrix product:
  A = MATMUL(B, C)
Shapes must
be identical
Shapes must match: SIZE(B, 2) == SIZE(C, 1)

## Slide 45: Intrinsic functions on arrays
Operating element-wise
  SQRT, SIN, COS, …, EXP, LOG, LOG10, …
Aggregating
  SUM, PRODUCT, COUNT, MAXVAL, MINVAL, ANY, ALL
Transform
  RESHAPE, TRANSPOSE
on arrays of LOGICAL
…
REAL(KIND=dp), DIMENSION(m, n) :: a REAL(KIND=dp), DIMENSION(m) :: col_sum
REAL(KIND=dp), DIMENSION(n) :: row_sum
REAL(KIND=dp) :: pos_sum
INTEGER :: nr_pos
…
col_sum = SUM(a, DIM=2)
row_sum = SUM(a, DIM=1)
pos_sum = SUM(a, MASK=a > 0.0_dp)
nr_pos = COUNT(a > 0.0_dp)
…

## Slide 46: Allocatable variables: motivation
Size can be determined at runtime
  only use as much memory as required
Can be deallocated
  only use memory while needed
Ideal for dynamics/semi-structured data types
  stack
  list
  graph
Requires user defined
types & pointers, see later

## Slide 47: Allocatable arrays
Declare 2D-array allocatable
Allocate memory for array
Always test whether allocated
Deallocate array
REAL(KIND=dp), DIMENSION(:, :), ALLOCATABLE :: a
INTEGER :: m, n, istat
m = …
n = …
ALLOCATE(a(m, n), STAT=istat)
DEALLOCATE(a, STAT=istat)
IF (.NOT. ALLOCATED(a)) THEN
…
END IF
allocate
use
deallocate
use only memory required at runtime!
free memory no longer required
can be omitted  auto-deallocation
C/C++
cfr. C malloc/free
IF (istat /= 0) THEN
…
END IF

## Slide 48: Pointers
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/Matrices
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/OOProgramming

## Slide 49: Pointers & targets
…
REAL(KIND=dp), DIMENSION(m, n), TARGET :: temp_1, temp_2
REAL(KIND=dp), DIMENSION(:, :), POINTER :: old_temp => NULL(), &
new_temp => NULL(), &
tmp => NULL()
…
old_temp => temp_1
new_temp => temp_2
DO iteration = 1, nr_iterations
DO j = 1, n
DO i = 1, m
new_temp(i, j) = 0.25_dp*(old_temp(i-1, j) + …)
END DO
END DO
…
tmp => new_temp
new_temp => old_temp
old_temp => tmp
END DO
…
initialize pointers to null
pointer assignment operator
use of pointers will prevent vectorization! fix with compiler flags: -fno-alias for Intel ifort

## Slide 50: Associations
…
REAL(KIND=dp), DIMENSION(:, :), ALLOCATABLE, TARGET :: temp
REAL(KIND=dp), DIMENSION(:, :), POINTER :: p_temp => NULL()
…
1 IF (ASSOCIATED(p_temp)) …
2 IF (ALLOCATED(temp)) …
3 p_temp => temp
4 IF (ASSOCIATED(p_temp)) …
5 ALLOCATE(temp(m, n))
6 IF (ALLOCATED(temp)) …
7 IF (ASSOCIATED(p_temp)) …
8 p_temp => temp
9 IF (ASSOCIATED(p_temp)) …
…
10 DEALLOCATE(temp)
11 IF (ASSOCIATED(p_temp)) …
12 IF (ASSOCIATED(p_temp, temp) …
13 p_temp => NULL()
14 IF (ASSOCIATED(p_temp)) …
…
.FALSE.
.FALSE.
.FALSE.
.FALSE.
.FALSE.
.TRUE.
.TRUE.
.FALSE.
.TRUE.

## Slide 51: User defined types
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/Functions
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/OOProgramming

## Slide 52: User defined types defined
Structure with multiple fields
Declaring variables
Using variables
…
TYPE :: rational
INTEGER :: num, denom, sign
END TYPE rational
…
…
TYPE(rational) :: a, b
…
…
a%num = 12; b%denom = 15; a%sign = 1
b%num = 5*a%num
…
C/C++
cfr. C struct

## Slide 53: Flexible data representations
Fields can have any type
Use user defined types + pointers + allocatable to create flexible data structures
  lists
  trees
  graphs
  ….
…
TYPE descriptive_stats
INTEGER :: n
REAL(KIND=sp) :: sum, mean, stddev
END TYPE descriptive_stats
…

## Slide 54: Procedures
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/Functions

## Slide 55: Arguments & scope
Variables declared in procedures are local
Call-by-reference semantics
  variables passed to procedures can be modified
  declare intent of arguments
    IN: argument is not modified
    OUT: argument's original value becomes undefined on entry to procedure, will be assigned to
    INOUT: argument's original value may be used, and modified
C/C++
call-by-value

## Slide 56: Subroutine definition
SUBROUTINE compute_stats(data, mean, stddev)
IMPLICIT NONE
REAL(KIND=sp), DIMENSION(:), INTENT(IN) :: data
REAL(KIND=sp), INTENT(OUT) :: mean, stddev
REAL(KIND=sp) :: s, s2
INTEGER :: n
n = SIZE(data)
s = SUM(data)
s2 = SUM(data*data)
mean = s/n
stddev = SQRT((s2/n - s**2))
END SUBROUTINE compute_stats
local variables
Intent of subroutine arguments:
IN: only read values OUT: only write new values
INOUT: both read value and update
Remember: in Fortran call-by-reference
C/C++
subroutine arguments
using IN arguments
assigning to OUT arguments

## Slide 57: Function definition
FUNCTION factorial(n) RESULT(f)
IMPLICIT NONE
INTEGER, INTENT(IN) :: n
INTEGER :: f
INTEGER :: i
f = 1
DO i = 2, n
f = f*i
END DO
END FUNCTION factorial
declaration of result name
declaration of result type
assignment to result variable
INTEGER FUNCTION factorial(n)
IMPLICIT NONE
INTEGER, INTENT(IN) :: n
INTEGER :: i
factorial = 1
DO i = 2, n
factorial = factorial*i
END DO
END FUNCTION factorial
declaration of result type
assignment of result to function name

## Slide 58: Keyword arguments
When procedure has many arguments, use keywords in call
  Advantage: order is irrelevant
…
REAL(KIND=sp) :: mu, sigma
REAL(KIND=sp), DIMENSION(size) :: v
…
CALL compute_stats(stddev=sigma, data=v, mean=mu)
…
remember: subroutines can only be used in a CALL statement!

## Slide 59: Optional arguments
SUBROUTINE print_vector(v, label)
IMPLICIT NONE
REAL(KIND=dp), DIMENSION(:), INTENT(IN) :: v
CHARACTER(LEN=*), OPTIONAL, INTENT(IN) :: label
IF (PRESENT(label)) THEN
PRINT '(2A)', label, ':'
END IF
PRINT '(F10.2)', v
END SUBROUTINE print_vector
…
REAL(KIND=dp), DIMENSION(size1) :: v1
REAL(KIND=dp), DIMENSION(size2) :: v2
…
CALL print_vector(v1)
…
CALL print_vector(v2, 'vector v2')
CALL print_vector(v2, label='vector v2')
…
without optional argument
with optional argument
better style
Optional arguments should come last

## Slide 60: Arrays & strings as arguments
Assumed shape arrays
Assumed length strings
FUNCTION compute_stats(x) RESULT(stats)
IMPLICIT NONE
REAL(KIND=dp), DIMENSION(:), INTENT(IN) :: x
TYPE(descriptive_stats) :: stats
stats%n = SIZE(x)
stats%sum = SUM(x)
stats%mean = stars%sum/stats%n
stats%stddev = SQRT((stats%sum**2 - SUM(x**2))/(stats%n - 1))
END FUNCTION compute_stats
shape assumed: 1D array, dimension unknown at compile time
determine dimensions in function at run time
SUBROUTINE print_vector(v, label)
…
CHARACTER(LEN=*), OPTIONAL, INTENT(IN) :: label
…
length assumed: string length unknown at compile time

## Slide 61: Pure functions
If all arguments are INTENT(IN), function is pure
Compiler can optimize/parallelize more easily
  e.g., in FORALL
PURE FUNCTION factorial(n) RESULT(f)
IMPLICIT NONE
INTEGER, INTENT(IN) :: n
INTEGER :: f
INTEGER :: i
f = 1
DO i = 2, n
f = f*i
END DO
END FUNCTION factorial
No side effects are permitted
(I/O, writing to variables from
outer scope)

## Slide 62: Elemental functions
Functions with scalar INTENT(IN) argument(s)
can be invoked on arrays, result is array
ELEMENTAL FUNCTION factorial(n) RESULT(f)
IMPLICIT NONE
INTEGER, INTENT(IN) :: n
INTEGER :: f
INTEGER :: i
f = 1
DO i = 2, n
f = f*i
END DO
END FUNCTION factorial
…
INTEGER, DIMENSION(n) :: input, output
…
output = factorial(input)
…
No side effects are permitted
(ELEMENTAL implies PURE)

## Slide 63: Elemental subroutines
Subroutine with scalar INTENT(INOUT) or INTENT(OUT) argument(s)
can be invoked on arrays
ELEMENTAL SUBROUTINE in_place_factorial(i)
IMPLICIT NONE
INTEGER, INTENT(INOUT) :: i
i = factorial(i)
END SUBROUTINE in_place_factorial
…
INTEGER, DIMENSION(n) :: a
…
CALL in_place_factorial(a)
…

## Slide 64: Elemental intrinsic procedures
Many intrinsic procedures are elemental
  SQRT
  SIN, COS,…
  EXP, LOG, LOG10,…
  RANDOM_NUMBER

## Slide 65: Recursive procedures
If defined recursively, must be declared explicitly
RECURSIVE FUNCTION factorial(n) RESULT(f)
IMPLICIT NONE
INTEGER, INTENT(IN) :: n
INTEGER :: f
INTEGER :: i
IF (n > 2) THEN
f = n*factorial(n-1)
ELSE
f = 1
END IF
END FUNCTION factorial
Recursive implementations may not be most efficient!

## Slide 66: Initialization of local variables
FUNCTION factorial(n) RESULT(f)
IMPLICIT NONE
INTEGER, INTENT(IN) :: n
INTEGER :: f, i, fac = 1
DO i = 2, n
fac = fac*i
END DO
f = fac
END FUNCTION factorial
0 1
1 1
2 2
3 12
4 288
Oops!?!
procedure local variables initialized in declaration retain value between calls
(implicit SAVE attribute)
cfr. C static local variables
C/C++

## Slide 67: Where to define procedures
In main program
Better: in modules
PROGRAM matrix_test
IMPLICIT NONE
…
REAL(KIND=dp), DIMENSION(m, n) :: A
…
CALL init_matrix(A)
…
CONTAINS
SUBROUTINE init_matrix(matrix)
…
END SUBROUTINE init_matrix
END PROGRAM matrix_test

## Slide 68: Modules
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/Functions
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/Matrices
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/OOProgramming

## Slide 69: Modules
Create modular code
  not executed directly
  contain declarations/definitions of
    data types
    variables
    procedures
  limit scope of data types/variables/procedures
    public versus private
  provide interface
Easy reuse of code
Design: keep related stuff together

## Slide 70: Module definition
MODULE matrix_ops USE :: precision_defs
IMPLICIT NONE
PRIVATE
REAL(KIND=dp), PARAMETER :: init = 1.0_dp
PUBLIC :: init_matrix, print_matrix
CONTAINS
SUBROUTINE init_matrix(A)
…
END SUBROUTINE init_matrix
…
END MODULE matrix_ops
declarations
definitions
public wherever used
MODULE precision_defs USE, INTRINSIC :: iso_fortran_env
IMPLICIT NONE
PRIVATE
INTEGER, PROTECTED :: dp
INTEGER, PROTECTED :: sp
… END MODULE matrix_ops
declarations
private to module
can be changed
in module, only read elsewhere

## Slide 71: Using modules
PROGRAM matrix_test
USE :: precision_defs
USE :: matrix_ops
IMPLICIT NONE
…
REAL(KIND=dp), DIMENSION(m, n) :: A
…
CALL init_matrix(A)
…
END PROGRAM matrix_test
public in precision_defs module
public in matrix_ops module
Everything in module that is public can be used
…
USE :: precision_defs, only : &
dp, single => sp
…
use sp as single to prevent name clash
list explicitly what is to be used

## Slide 72: Modules & user defined types
MODULE rationals
… PRIVATE
TYPE, PUBLIC :: rational
PRIVATE
INTEGER :: num, denom, sign
END TYPE rational
PUBLIC :: rat_create, rat_add, rat_mul, rat_print
CONTAINS
…
FUNCTION rat_mul(a, b) RESULT(c) IMPLICIT NONE
TYPE(rational), INTENT(IN) :: a, b TYPE(rational) :: c
c%denom = ABS(a%denom*b%denom)
c%num = ABS(a%num*b%num)
c%sign = a%sign*b%sign
CALL rat_simplify(c)
END FUNDION rat_mul
…
END MODULE rationals
fields are private
fields can be accessed
in module

## Slide 73: "Constructor"
TYPE(rational) FUNCTION rat_create(n, d)
IMPLICIT NONE
INTEGER, VALUE :: n, d
INTEGER :: n_act, d_act, g
IF (d == 0) THEN
WRITE (UNIT=error_unit, FMT='(A)') &
"# error: denominator must be non-zero"
STOP
END IF
rat_create%sign = SIGN(1, n*d)
n = ABS(n)
d = ABS(d)
g = gcd(n, d)
rat_create%num = n/g
rat_create%denom = d/g
END FUNCTION rat_create
enforce call-by-value semantics

## Slide 74: Working with rationals
PROGRAM rational_test
USE :: rationals
IMPLICIT NONE
…
TYPE(rational) :: a, b, c
…
a = rat_create(3, 5)
b = rat_create(-1, 2)
c = rat_mul(a, b)
rat_print(c)
…
END PROGRAM rational_test
Not very elegant

## Slide 75: Interface for constructor
MODULE rationals
… INTERFACE rational
MODULE PROCEDURE rat_create
END INTERFACE rational
PUBLIC :: rat_add, rat_mul, rat_print
…
END MODULE rationals
PROGRAM rational_test
USE :: rationals
IMPLICIT NONE
…
TYPE(rational) :: a, b, c
…
a = rational(3, 5)
b = rational(-1, 2)
c = rat_mul(a, b)
rat_print(c)
…
END PROGRAM rational_test
Note: slowly moving into OO country!

## Slide 76: Interface for operator
MODULE rationals
… INTERFACE operator(*)
MODULE PROCEDURE rat_mul
END INTERFACE
PUBLIC :: rat_add, operator(*), rat_print
…
END MODULE rationals
PROGRAM rational_test
USE :: rationals
IMPLICIT NONE
…
TYPE(rational) :: a, b, c
…
a = rational(3, 5)
b = rational(-1, 2)
c = a*b
rat_print(c)
…
END PROGRAM rational_test
Operator overloading allows for domain-specific code

## Slide 77: Overloading
MODULE rationals
… INTERFACE operator(*)
MODULE PROCEDURE rat_mul, int_rat_mul
END INTERFACE
PUBLIC :: rat_add, operator(*), rat_print
…
CONTAINS
…
FUNCTION int_rat_mul(i, a) RESULT(b) IMPLICIT NONE
INTEGER, VALUE :: i
TYPE(rational), INTENT(IN) :: a TYPE(rational) :: b
b = rational(i*a%sign*a%num, a%denom)
END FUNDION int_rat_mul
…
END MODULE rationals
signature differs
from rat_mul
overloaded operator

## Slide 78: Using overloaded operator
PROGRAM rational_test
USE :: rationals
IMPLICIT NONE
…
TYPE(rational) :: a, b, c, d
…
a = rational(3, 5)
b = rational(-1, 2)
…
c = a*b
…
d = 3*a
…
END PROGRAM rational_test
call to rat_mul
call to int_rat_mul

## Slide 79: Classes
Class = user defined type
  object attributes: elements of type
  object methods: procedures contained in type
Inheritance = extend user defined type
  declare additional elements
  override/declare/define additional procedures

## Slide 80: Base class
…
TYPE, PUBLIC :: node_type
PRIVATE
REAL(KIND=sp) :: value = 0.0_sp
CLASS(node_type), POINTER :: left => null(), & right => null()
CONTAINS
…
PROCEDURE, PUBLIC :: set_left
…
END TYPE node_type
…
SUBROUTINE set_left(node, child)
IMPLICIT NONE
CLASS(node_type), INTENT(INOUT) :: node
CLASS(node_type), TARGET, INTENT(IN) :: child
node%left => child
END SUBROUTINE set_left
…
CLASS:  type  extended types

## Slide 81: Derived class
…
TYPE, EXTENDS(node_type), PUBLIC :: id_node_type
PRIVATE
INTEGER :: id = 1
CONTAINS
…
PROCEDURE, PUBLIC :: get_id
…
END TYPE id_node_type
…
FUNCION get_id(node) RESULT(id)
IMPLICIT NONE
CLASS(id_node_type), INTENT(IN) :: node
INTEGER :: id
id = node%id
END FUNCTION get_id
…
base class
new element(s), procedure(s)
must be class with ID

## Slide 82: Overriding procedures
…
FUNCTION new() RESULT(node)
IMPLICIT NONE
CLASS(node_type), POINTER :: node
INTEGER :: status
ALLOCATE(node, STAT=status, & SOURCE=node_type(0.0_sp, null(), null()))
…
END FUNCTION new …
node_type definition
…
FUNCTION new() RESULT(node)
IMPLICIT NONE
CLASS(node_type), POINTER :: node
INTEGER :: status
global_id = global_id + 1
ALLOCATE(node, STAT=status , & SOURCE=id_node_type(id=global_id))
…
END FUNCTION new
…
id_node_type definition
Full fledged OO
PROCEDURE, NOPASS, PUBLIC :: new
class method

## Slide 83: Procedure type definitions
Declare function to compute quadrature of
MODULE quad_function_interface
INTERFACE
FUNCTION quad_function_type(x) RESULT(f)
USE precision_defs
IMPLICIT NONE
REAL(KIND=dp), INTENT(IN) :: x
REAL(KIND=dp) :: f
END FUNCTION quad_function_type
END INTERFACE
END MODULE quad_function_interface
procedure signature
procedure type name

## Slide 84: Procedure as argument
Define function that computes quadrature
MODULE quad_mod
IMPLICIT NONE
PRIVATE
PUBLIC :: quad
CONTAINS
FUNCTION quad(f, a, b) RESULT(q_f)
USE precision_defs
USE quad_function_interface
IMPLICIT NONE
PROCEDURE(quad_function_type) :: f
REAL(KIND=dp), INTENT(IN) :: a, b
REAL(KIND=dp) :: q_f
…
END FUNCTION quad
END MODULE quad_mod
procedure type

## Slide 85: Using higher order procedures
Calling function that computes quadrature
PROGRAM quad_test
USE precision_defs
USE quad_mod
IMPLICIT NONE
PRINT *, quad(f, -1.0_dp, 1.0_dp)
CONTAINS
REAL(KIND=dp) FUNCTION f(x)
IMPLICIT NONE
REAL(KIND=dp), INTENT(IN) :: x
f = EXP(x)*COS(x)
END FUNCTION f
END PROGRAM quad_test
same signature as quad_function_type

## Slide 86: Internal procedures
Procedures local in procedures
ELEMENTAL FUNCTION on_line(x, y) RESULT(is_on_line)
IMPLICIT NONE
REAL(KIND=sp), INTENT(IN) :: x, y
LOGICAL :: is_on_line
REAL(KIND=sp) :: y_exp
y_exp = line(x)
is_on_line = equal(y, y_exp)
CONTAINS
PURE FUNCTION equal(a, b) RESULT(is_equal)
IMPLICIT NONE
REAL(KIND=sp), INTENT(IN) :: a, b
LOGICAL :: is_equal
is_equal = ABS(a - b) < epsilon
END FUNCTION equal
END FUNCTION on_line
internal function, can only be called from within on_line
One level of internal procedures only!
never use == or /= to compare REAL

## Slide 87: File I/O
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/IO

## Slide 88: Files & records
Two types of records
  data records
    formatted: human readable
    unformatted: binary
  endfile record
File = sequence of data records + endfile record
  either formatted, or unformatted, not both
  two types
    internal: in-memory file
    external: on file system, e.g., on disk

## Slide 89: File access
Three modes
  sequential
  direct access
    all records must have same length
    access by record number
    only for external files
  stream access
    allows to reposition inside the file
    no record-based I/O, better portability
Files associated to units

## Slide 90: Standard I/O
Units defined in iso_fortran_env
  USE, INTRINSIC :: iso_fortran_env
Standard input
  input_unit
Standard output
  output_unit
Standard error
  error_unit

## Slide 91: Opening a file
…
OPEN( &
UNIT=file_unit, &
FILE=file_name, &
ACCESS='sequential', &
ACTION='readwrite', &
STATUS='new', &
FORM='formatted', &
IOSTAT=istat, &
IOMSG=message &
)
…
file handle, constant INTEGER
file name, string
access method: sequential, direct, stream
action: read, write, readwrite
'
file status: new, old, replace, scratch
record format: formatted, unformatted
INTEGER variable: 0 for success, non-0 for failure
string variable: error message on failure
FILE must be present if STATUS is old, new, replace,
must not be present if STATUS is scratch
POSITION must be present if STATUS is old and ACCESS is sequential
if STATUS is new, replace, ACTION must not be read,
if STATUS is scratch, ACTION must be readwrite

## Slide 92: Closing a file
…
CLOSE( &
UNIT=file_unit, &
IOSTAT=istat, &
IOMSG=message &
)
…
close STATUS can be keep if open STATUS is scratch

## Slide 93: Check status!
Check I/O status for all I/O operations
  OPEN, CLOSE, READ, WRITE, …
…
IF (istat /= 0) THEN
WRITE (UNIT=error_unit, FMT="('# error: ', A)")) message
STOP
END IF
…
Always, always check IOSTAT!!!

## Slide 94: (Minimalistic) record formats
List of specifiers
  real: Fw.d, Ew.d
  integer: Iw
  characters: Aw
  logical: Lw
  literal string
  sublists
  repetitions
"(I5, ':', 2(E10.2, ';'), E10.2)"
"(I5, ':', E10.2, ';', E10.2, ';', E10.2)"

If record width too small: *********
Use same format specification for write and read!
Repetition, can be *

## Slide 95: Writing to a file
Unformatted records
Formatted records
…
WRITE ( &
UNIT=file_unit, &
IOSTAT=istat, &
IOMSG=message &
) x, y, z
…
…
WRITE ( &
UNIT=file_unit, &
FMT='(3F25.15)', &
IOSTAT=istat, &
IOMSG=message &
) x, y, z
…

## Slide 96: Reading from a file
Unformatted records
Formatted records
…
READ ( &
UNIT=file_unit, &
IOSTAT=istat, &
IOMSG=message &
) x, y, z
…
…
READ ( &
UNIT=file_unit, &
FMT='(3F25.15)', &
IOSTAT=istat, &
IOMSG=message &
) x, y, z
…

## Slide 97: File positioning
Go to beginning of file
  REWIND(UNIT=file_unit, & IOSTAT=istat, & IOMSG=message
Determine current position
  INQUIRE(UNIT=file_unit, POS=file_pos)
Read at position
  READ(UNIT=file_unit, POS=file_pos, …) …
Write at position
  WRITE(UNIT=file_unit, POS=file_pos, …) …
stream I/O

## Slide 98: Inquiries
Inquiry by unit, e.g.,
  INQUIRE(UNIT=file_unit, & POS=file_pos)
  INQUIRE(UNIT=file_unit, & NAME=file_name)
Inquiry by name, e.g.,
  INQUIRE(FILE=file_name, & EXIST=file_exists)

## Slide 99: Stream write
…
INTEGER, PARAMETER :: file_unit = 9
REAL(KIND=dp), DIMENSION(nr_data) :: x
…
OPEN(UNIT=file_unit, FILE=file_Name, ACCESS='stream', &
ACTION='write', STATUS='replace', & FORM='unformatted', IOSTAT=istat, IOMSG=msg)
…
WRITE (UNIT=file_unit, IOSTAT=istat, IOMSG=msg) x
…
CLOSE(UNIT=file_unit, IOSTAT=istat, IOMSG=msg)
…
complete array written at once
If possible, write large chunks of data at once

## Slide 100: Stream read
…
INTEGER, PARAMETER :: file_unit = 9
REAL(KIND=dp) :: x
…
OPEN(UNIT=file_unit, FILE=file_Name, ACCESS='stream', &
ACTION='read', STATUS='old', & FORM='unformatted', IOSTAT=istat, IOMSG=msg)
…
DO WHILE (.TRUE.)
READ (UNIT=file_unit, IOSTAT=istat, IOMSG=msg) x
IF (is_iostat_end(istat)) THEN
EXIT
END IF
…
END DO
…
CLOSE(UNIT=file_unit, IOSTAT=istat, IOMSG=msg)
…
tests whether end of file was reached
at end of file, x is undefined: don't use value!

## Slide 101: Command line interaction
https://github.com/gjbex/Fortran-for-programmers/tree/master/source-code/Miscellaneous

## Slide 102: Command line arguments
Number of command line arguments:
  COMMAND_ARGUMENT_COUNT()
Get a command line argument, e.g., second:
  CALL GET_COMMAND_ARGUMENT(2, value)
…
INTEGER, PARAMETER :: max_len = 1024, expected_count = 3
CHARACTER(LEN=max_len) :: value
…
IF (COMMAND_ARGUMENT_COUNT() /= expected_count) THEN
…
END IF
CALL GET_COMMAND_ARGUMENT(1, value)
…
Tip: make your life easy, use parameter-weaver https://github.com/gjbex/parameter-weaver http://parameter-weaver.readthedocs.org/en/latest/

## Slide 103: Converting strings
To convert command line arguments, use internal files
…
REAL(KIND=dp) :: x
…
CALL GET_COMMAND_ARGUMENT(1, value)
READ (value, FMT='(E25.15)', &
IOSTAT=istat, IOMSG=message) x
IF (status /= 0) THEN
WRITE (UNIT=error_unit, FMT='(2A)') &
'# error: ', trim(message)
STOP
END IF
…
format string for real number

## Slide 104: Environment variables
Get an environment variable, e.g., HOME
  GET_ENVIRONMENT_VARIABLE('HOME', value)
…
INTEGER, PARAMETER :: max_len = 1024
CHARACTER(LEN=max_len) :: value
INTEGER :: status
…
CALL GET_ENVIRONMENT_VARIABLE('HOME', value, status=status)
IF (status > 0) THEN
! not defined, do something like initialize to default
…
ELSE IF (status < 0) THEN
! environment variable longer than length of value
! value contains truncated environment variable
…
STOP
END IF
…

## Slide 105: Return codes
Return codes allow command lines scripts to check for (un)successful execution
Use STOP with number
…
INTEGER, PARAMETER :: file_not_found_err = 1, &
not_integer_err = 2, &
negative_arg_err = 3
…
IF (…) THEN
WRITE (UNIT=error_unit, FMT='(A)') error_message
STOP file_not_found_err
END IF
…
$ echo $?
1

## Slide 106: Conclusion & further reading

## Slide 107: Conclusions
Fortran 2003/2008 is a very modern programming language
Fortran has been designed for scientific computing
High level language, good compilers = highly efficient code
Much more to explore, e.g., object-oriented or parallel programming

## Slide 108: References
Chapman, S. Fortran 95/2003 for scientists and engineers McGraw-Hill, 2007
Metcalf, M., Reid, J. & Cohen, M. Modern Fortran explained Oxford University Press, 2011
Clerman, N. S. & Spector, W. Modern Fortran: style and usage Cambridge University Press, 2011
Brainerd, W. S. Guide to Fortran 2003 programming Springer, 2009
Fortran best practices http://www.fortran90.org/src/best-practices.html

## Slide 109: Appendix

## Slide 110: Fortran compilers
GCC's gfortran is more strict than Intel's ifort
  eliminate warnings generated by both compilers
Compile with no implicits allowed:
  ifort: -implicitnone
  gfortran: -fimplicit-none
While developing, switch on array bound checking at runtime
  ifort: -check bounds
  gfortran: -fbounds-check
Check for not explicitly initialized variables
  ifort: -check uninit
  gfortran: -finit-integer=-1000 (or whatever) -finit-real=nan
Be careful using latest language features
  may not be (reliably) implemented yet
incurs performance penalty!